## Slide 1
EE2003: Computer Organization & Assembly Language
2 – Architecture Overview

## Slide 2
Outline
  The Components of Microcomputer System
    The CPU
      Registers
    Memory
      Types: RAM, ROM, Cache
      Memory Organization & Segmentation
    System Bus
      Data, Address & Control
2
Von Neumann Architecture
Notes: 2

## Slide 3
The CPU

## Slide 4
CPU
2
Brain of Computer; controls all operations
  Uses Memory Circuits to store information
  Uses I/O Circuits to communicate with I/O Devices
Executes programs stored in memory
  System programs
  Application programs
Instruction Set: Instructions performed by CPU
Two main components:
  Execution Unit (EU)
  Bus Interface Unit (BIU)

## Slide 5
Execution Unit (EU)
4
Purpose: Execute instructions
Contains ALU (Arithmetic & Logic Unit)
  To perform arithmetic (+, -, x,/) and logic (AND, OR, NOT) operations.
The data for the operations are stored in circuits called Registers.
A register is like a memory location except that it is referred by a name not a number (address).
EU uses registers for:
  Storing data.
  Holding operands for ALU
  To reflect result of a computation – FLAG register
Notes: Register details covered in later slides
5

## Slide 6
Bus Interface Unit (BIU)
4
Facilitates communication between the EU and the memory or I/O circuits.
Responsible for transmitting address, data and control signals on the buses.

## Slide 7
Internal Bus
6
The EU and BIU are connected by an internal bus and they work together.
While EU is executing, the BIU fetches up to six bytes of the next instruction and places them in the instruction queue.
  Instruction Pre-fetch
  Purpose: Speed up the processor
If the EU needs to communicate with memory or the peripherals, the BIU suspends instruction pre-fetch and performs the needed operations.

## Slide 8
7
Intel 8086 Microprocessor Organization

## Slide 9
Registers

## Slide 10
Registers
Registers are high-speed storage locations inside the microprocessor.
Designed to be accessed at much higher speed than conventional memory.
Registers are classified according to the functions they perform.
General Types of Registers:
  Data Registers: To hold data for an operation.
  Address Registers: To hold the address of an instruction or data.
  Status/Flag Register: keeps the current status of the processor or result of an arithmetic operation.
7

## Slide 11
7
8086 Internal registers 16 bits (2 bytes each)
AX, BX, CX and DX are two
bytes wide and each byte can
be accessed separately
These registers are used as
memory pointers.
Segment registers are used
as base address for a segment
6 status; 3 control ; 7 unused

## Slide 12
General Purpose/Data Registers
Following four registers are available to the programmer for general data manipulation:
AX (Accumulator): Used in arithmetic, logic and data transfer instructions. Also required in multiplication, division and input/output operations.
BX (Base): It can hold a memory address that points to a variable.
CX (Counter): Act as a counter for repeating or looping instructions. These instructions automatically repeat and decrement CX and quit when equals to 0.
DX (Data): It has a special role in multiply and divide operations. Also used in input/output operations.
7

## Slide 13
Segment Registers
Store addresses of instruction and data in memory.
These values are used by the processor to access memory locations.
CS (Code): Defines the starting address of the section of memory holding code.
DS (Data): Defines the section of memory that holds most of the data used by programs.
ES (Extra): This is an additional data segment that is used by some of the string instructions.
SS (Stack): It defines the area of the memory used for stack
7

## Slide 14
Pointers and Index Registers
These can be accessed only as 16 bit registers.
IP - instruction pointer: Always points to next instruction to be executed. IP register always works together with CS segment register and it points to currently executing instruction.
SI - source index register: Can be used for pointer addressing of data. Offset address relative to DS
DI - destination index register: Can be used for pointer addressing of data . Offset address relative to ES
SI and DI used in string movement instructions.
SP and BP are used to access data inside the stack segment
BP - base pointer: Primarily used to access parameters passed via the stack. Offset address relative to SS
SP – stack pointer: Always points to top item on the stack. Offset address relative to SS
7

## Slide 15
80386 Extended Registers
The 80386/80486 processor contain 32-bit registers which greatly improve the efficiency of program that take advantage of them.
  EAX, EBX, ECX, EDX,
  EFLAGS
  EIP
  EBP, ESP, ESI, EDI.
7

## Slide 16
Memory

## Slide 17
Each 1 or 0 is called a bit.
Group of 4 bits = Nibble
Group of 8 bits = Byte
Group of 16 bits = Word
Group of 32 bits = Double words
Bits, Bytes and Double words
7

## Slide 18
Common Prefixes
7

## Slide 19
Memory
Information processed by the computer is stored in its memory.
  Program
  Data
Not all accumulated information is needed by the CPU at the same time
  Therefore, it is more economical to use low-cost storage devices to serve as a backup for storing the information that is not currently used by CPU
Memory Operations:
  Read (Fetch contents of a location)
  Write (Store data at a location)
19
Von Neumann Architecture

## Slide 20
Memory Hierarchy
<number>

## Slide 21
Main Memory
<number>
Most of the main memory in a general purpose computer is made up of RAM integrated circuits chips, but a portion of the memory may be constructed with ROM chips
Memory Circuits:
  RAM
    Program Data and Instructions
    Read and Write
  ROM
    Used for storing an initial program called bootstrap loader, which is required to start the computer software operating when power is turned off.
    Only Read

## Slide 22
Cache
<number>
A special very-high-speed memory called cache is used to increase the speed of processing by making current programs and data available to the CPU at a rapid rate.
To reduce memory access time thus program execution time.
Notes: 22

## Slide 23
Memory Organization
Memory is organized into a collection of bytes.
Each byte is identified by a number – Address
  Number of bits in an address depends on the processor
  Example:- Intel 8086: 20-bit address, Intel 80286: 24-bit address
Data stored in a memory byte – Contents
23

## Slide 24
Contd..
23
Number of bits used in the address determines the number of bytes that can be accessed by the processor.
Example: If processor uses 20-bit address, it can access 220 = 1048576 bytes = 1 MB of memory
Question: If processor uses 24-bit address, how many bytes of memory can be accessed?
Notes: 24

## Slide 25
Program Segments
A typical machine language program is loaded into following different memory segments:
  Code Segment
  Data Segment
  Stack Segment
Stack is a data structure used by processor to implement procedure calls.
24

## Slide 26
System Bus

## Slide 27
What is a Bus?
A communication pathway connecting two or more devices
Often grouped
  A number of channels in one bus
  e.g. 32 bit data bus is 32 separate single bit channels
24
CPU
Memory
I/O
Address Bus
Control Bus
Data Bus
Notes: <number>

## Slide 28
Data Bus
Carries data
  Remember that there is no difference between “data” and “instruction” at this level
Width is a key determinant of performance
  8, 16, 32, 64 bit
24
Notes: <number>

## Slide 29
Address bus
Identify the source or destination of data
  e.g. CPU needs to read an instruction (data) from a given location in memory
Bus width determines maximum memory capacity of system
  e.g. 8080 has 16 bit address bus giving 64k address space
24
Notes: <number>

## Slide 30
Control Bus
Control and timing information
  Memory read/write signal
  Interrupt request
  Clock signals
24
Notes: <number>

## Slide 31
Types of Transfer
Memory to Processor
Processor to Memory
I/O to Processor
Processor to I/O
I/O to and from Memory
24

## Slide 32
Interconnection Structure
Memory
  N words of equal length, each word having a unique address
  Unit of Transfer (read/Write): Word
  Operation: Read/Write indicated by Control Signal
  Location of operation specified by an address
I/O Module
  Two operations: read and write
  May control other external devices
  Port: interface between I/O module and device
  Able to send interrupt signal to CPU
24

## Slide 33
Contd..
  CPU
  Reads in instruction and data
  Writes out data
  Uses control signal to control all operations
  Receives interrupt signal
24

## Slide 34
24
Address
Data Read
Data Write
Interrupt Signals